Table 1. Examples of variables that are used in systems modelling in engineering and proposed relation to the effort-resistance-flow image schema. In each of these systems, we can identify effort and flow variables and also resistances.

| Domain | Effort (symbol [SI unit]) | Flow (symbol [SI unit]) | Resistance | Prototypical system |
| --- | --- | --- | --- | --- |
| Linear mechanics | Force (F [N]) | Velocity (v []) | Mechanical resistance (Rasmussen, 1994) |  |
| Electric circuits | Voltage (U [V]) | Current (I [A]) | Electrical resistance |  |
| Hydrodynamics | Pressure (P [Pa]) | Volumetric flow rate (Q []) | Pipe resistance (Lautrup, 2011) |  |
| Embodied | Kinaesthetic sensation of applying effort | Kinaesthetic sensation of flow | Felt resistance |  |